## Slide 1
September 2026
Dipartimento di Elettronica, Informazione e Bioingegneria
Politecnico di Milano
Risk-Adaptive Neurosymbolic Intent Planning for Optical Networks
A Pre-Deployment Decision Mechanism with Joint Semantic and QoT Assessment
Candidate: Felipe Abadía
Academic Advisor: Prof. Massimo Tornatore
Dipartimento di Elettronica, Informazione e Bioingegneria — Politecnico di Milano
Notes: [Estimated Time]: 30s
[Key Message]: Welcome the committee and state the thesis research focus.
[Spoken Script]: Good morning members of the committee and Professor Tornatore. Today I present my Master's thesis entitled "Risk-Adaptive Neurosymbolic Intent Planning for Optical Networks: A Pre-Deployment Decision Mechanism with Joint Semantic and QoT Assessment". In this work, we address the challenge of translating high-level operator intent into physically feasible optical configurations using a fail-fast, neurosymbolic pre-deployment pipeline.
[Bridge to Next Slide]: Let us begin with the specific roadmap of problems and solutions covered in this presentation.

## Slide 2
POLITECNICO DI MILANO
2
OUTLINE
[Problem 1] The Optical Intent Planning Bottleneck
Physical-layer constraints, token saturation, and hallucinated routing in optical backbones
[Architecture] Neurosymbolic Intent Planning Pipeline
Decoupling probabilistic reasoning (NL to PDDL) from deterministic solvers and physics tools
[Mechanism] Pre-Deployment Risk Gates: Semantic & Physical Validation
Sequential fail-fast decision via Layer 1/2 semantic gate (U_sem) and GN-model QoT gate
[Evaluation] Experimental Testbed Validation on 17-Node Optical Topology
Benchmarking safety, human intervention reduction, and orchestration latency against baselines
[Outlook] Key Takeaways, System Guarantees & Future Directions
Summary of thesis contributions, operational guarantees, and extension to joint compute scheduling
Notes: [Estimated Time]: 50s
[Key Message]: Present a thesis-specific narrative rather than a generic table of contents.
[Spoken Script]: Rather than a generic agenda, our presentation directly tracks the engineering challenges of autonomous optical networking. We begin by examining why general-purpose LLMs fail when controlling optical backbones. Next, we present our neurosymbolic architecture that cleanly separates natural language reasoning from optical physics. We then delve into the pre-deployment risk gates that protect the physical network before showing experimental validation on a 17-node optical topology and concluding with our primary takeaways.
[Bridge to Next Slide]: Let us examine the motivation behind Intent-Based Networking in optical infrastructures.

## Slide 3
POLITECNICO DI MILANO
3
Motivation: The Vision of Intent-Based Optical Networks
Operational Paradigm Shift
• Optical backbones carry terabits of core traffic across ROADM networks
• Traditional workflow: manual CLI scripts and complex RESTConf payloads
• Human configuration delays lightpath provisioning by hours or days
• Goal: Transition to autonomous Intent-Based Networking (IBN)
• Allow network operators to express high-level operational goals naturally
The Operational Promise
• High-level abstraction: specify WHAT is needed, not HOW to configure it
• Example: 'Establish a 400G lightpath between Milan and Rome avoiding L2'
• Autonomous translation into validated physical lightpaths
• Reduces human configuration error across multi-vendor optical links
• Critical challenge: Optical networks do not tolerate probabilistic errors
Notes: [Estimated Time]: 55s
[Key Message]: The promise of autonomous IBN is compelling, but optical networks impose strict physical constraints.
[Spoken Script]: Optical networks form the backbone of modern telecommunications, carrying terabits of traffic across core routes. Traditionally, provisioning lightpaths requires expert network operators to manually write vendor-specific RESTConf payloads or CLI scripts. Intent-Based Networking promises to revolutionize this by allowing operators to express high-level operational goals in natural language. While this vision is promising, direct deployment of Large Language Models to optical control planes exposes critical vulnerabilities.
[Bridge to Next Slide]: Let us look at a concrete illustrative failure example to see why.

## Slide 4
POLITECNICO DI MILANO
4
Illustrative Failure: Why Standard LLMs Break Optical Backbones
Challenge 1: Token Budget Saturation
• Full optical topology payloads (RESTConf JSON) exceed LLM context budgets
• In a 100-node core network, telemetry dumps consume tens of thousands of tokens
• Induces severe 'lost-in-the-middle' attention degradation
• Result: The LLM drops explicit user constraints such as link exclusion rules
• High API token cost and unpredictable prompt execution times
Challenge 2: Hallucinated Physics
• LLMs are probabilistic text predictors, not optical physics calculators
• Incapable of computing Generalized Signal-to-Noise Ratio (GSNR)
• Ignore nonlinear fiber Kerr effects and EDFA noise accumulation
• Result: Proposes lightpaths with unfeasible optical Quality of Transmission
• Causes severe traffic drop or optical controller rejection upon deployment
Notes: [Estimated Time]: 60s
[Key Message]: Standard LLMs cannot calculate optical physics and choke on massive topology payloads.
[Spoken Script]: Consider what happens if an operator asks a standard LLM to provision a 400G demand. First, we face Token Budget Saturation: dumping full topology states with hundreds of ROADMs and EDFA amplifier parameters degrades the LLM's attention, causing it to drop explicit constraints like link exclusions. Second, and more dangerously, LLMs suffer from Hallucinated Physics. Because they predict text probabilities rather than calculating nonlinear optical impairments, they will confidently propose routes that drop light below the required GSNR threshold, leading to service disruption.
[Bridge to Next Slide]: This fundamental gap defines our formal problem statement.

## Slide 5
POLITECNICO DI MILANO
5
Problem Statement: Inputs, Constraints & Objectives
1. Given Inputs
• Unstructured Natural Language intent from operator
• Physical topology graph G(V, E) via RESTConf
• Link fiber parameters: span lengths, attenuation
• EDFA amplifier gains and noise figures
• Transponder specs: baud rates, modulation formats
2. Constraints
• Semantic alignment: formal model matches intent
• Uncertainty bounded: U_sem <= tau_sem
• Optical GSNR exceeds modulation threshold
• Receiver power satisfies sensitivity: P_rx >= P_min
• Zero spectral overlap and wavelength collision
3. Objectives
• Zero unfeasible routes reaching controller
• Fail-fast pre-deployment validation pipeline
• Selective, risk-proportional HITL engagement
• Sub-second deterministic computation time
• Auditable planning report for network engineers
Notes: [Estimated Time]: 60s
[Key Message]: Formally state the problem across three distinct pillars: inputs, constraints, and objectives.
[Spoken Script]: To tackle this challenge rigorously, we formalize the problem into three concrete pillars. Our system receives an unstructured operator intent, the physical topology graph G(V, E), and optical layer parameters. It must satisfy two orthogonal constraint classes: semantic consistency to prevent intent drift, and deterministic optical physics, specifically GSNR and receiver power thresholds. Our core objective is simple yet strict: ensure zero physically unfeasible configurations ever reach the network controller, while engaging the operator only when genuine ambiguity exists.
[Bridge to Next Slide]: To achieve this, we introduce our core neurosymbolic architectural philosophy.

## Slide 6
POLITECNICO DI MILANO
6
Proposed Solution: Neurosymbolic Decoupling
Core Architectural Principle
• LLMs Reason, Deterministic Tools Calculate
• Prohibit LLMs from performing graph routing or arithmetic
• Constrain the LLM strictly to formal linguistic translation
• Natural Language is parsed into formal PDDL constraints
• Path computation delegated to Yen's KSP graph algorithms
• Physical validation delegated to analytical GN-model engine
Four Core Contributions
• 1. Neurosymbolic Pipeline: High-accuracy NL-to-PDDL translation
• 2. Scoped Optical GraphRAG: k-hop neighborhood extraction
• 3. Pre-Deployment Risk Gates: Joint U_sem and QoT validation
• 4. Production Orchestration: LangGraph StateGraph engine
• Guarantees provable physical safety before configuration push
Notes: [Estimated Time]: 55s
[Key Message]: State the thesis contributions explicitly: decoupling probabilistic reasoning from deterministic calculations.
[Spoken Script]: Our core architectural principle is: 'LLMs reason, deterministic tools calculate'. We forbid the LLM from performing math or path exploration. Instead, the LLM acts solely as a semantic translator, converting natural language into formal Planning Domain Definition Language, or PDDL. This enables our four key contributions: a neurosymbolic pipeline, a scoped Optical GraphRAG mechanism, sequential pre-deployment risk gates, and an auditable LangGraph state machine.
[Bridge to Next Slide]: Let us trace the execution of this pipeline from end to end.

## Slide 7
POLITECNICO DI MILANO
7
End-to-End System Architecture & Pipeline Flow
Phase 1 Intent Ingest & Optical RAG
Enrich operator intent with ITU-T optical grid standards and transponder modes
Phase 2 PDDL Intent Parsing
Translate enriched intent into formal Planning Domain Definition Language constraints
Phase 3 Semantic Gate (U_sem)
Evaluate CFG regex syntax and Reverse Prompting disagreement to catch hallucinations early
Phase 4 Symbolic Solver & GraphRAG
Extract scoped k-hop subtopology and generate K-Shortest Paths via NetworkX
Phase 5 QoT Physics Validation
Compute deterministic GSNR and receiver power P_rx using Python GN-model
Phase 6 Risk-Adaptive Decision Gate (RADG)
Execute piecewise decision function D(U_sem, QoT_valid) -> Auto-Approve / Replan / Clarify
Phase 7 Plan Synthesizer
Generate auditable planning report with verification traces and testbed deployment commands
Notes: [Estimated Time]: 60s
[Key Message]: Walk through the clean 7-phase pipeline, highlighting the sequential fail-fast flow.
[Spoken Script]: Here we see the complete 7-phase execution pipeline. The operator's intent enters Phase 1 where it is enriched with optical standards. In Phase 2, the LLM generates PDDL constraints. Crucially, before running heavy graph solvers or physics tools, Phase 3 evaluates semantic uncertainty. If semantically sound, Phase 4 extracts candidate routes via symbolic graph algorithms. Phase 5 evaluates physical feasibility using a deterministic GN-model. Finally, the Risk-Adaptive Decision Gate verifies physical safety before synthesizing the final auditable report.
[Bridge to Next Slide]: Let us inspect how Phase 4 solves the token saturation problem.

## Slide 8
POLITECNICO DI MILANO
8
Overcoming Token Saturation: Scoped Optical GraphRAG
The Problem: Topology Bloat
• Full topology dumps overwhelm LLM context windows
• Raw JSON contains excessive telemetry: ROADM ports, EDFAs, fibers
• Causes severe attention degradation on key operational constraints
• Linear increase in inference latency and financial token cost
• Fragile prompt structures prone to truncation and context loss
Deterministic k-hop Subtopology Scoping
• Graph engine extracts only the k-hop neighborhood between endpoints
• Filters out irrelevant core subnets, links, and unused transponders
• Reduces prompt token payload by over 75%
• O(V + E) graph traversal executes in sub-millisecond Python code
• Guarantees sharp LLM attention focus on active optical constraints
Notes: [Estimated Time]: 50s
[Key Message]: Scoped GraphRAG extracts only relevant k-hop subtopologies, eliminating attention degradation.
[Spoken Script]: To solve token budget saturation, we implement Scoped Optical GraphRAG. Instead of flooding the LLM context with hundreds of network nodes and links, our deterministic graph engine extracts only the k-hop neighborhood bounding the source and destination. This reduces the prompt token footprint by over 75 percent, completely eliminating lost-in-the-middle phenomena while keeping the graph search computationally light.
[Bridge to Next Slide]: Now let us examine how we eliminate semantic drift before any physics calculations occur.

## Slide 9
POLITECNICO DI MILANO
9
Overcoming Semantic Drift: Reverse Prompting & HITL
Two-Layer Semantic Uncertainty (U_sem)
• Layer 1 (Structural): Context-Free Grammar (CFG) regex validator
• Instantly rejects hallucinated predicates or malformed PDDL syntax
• Layer 2 (Semantic): Reverse Prompting reconstructs NL from PDDL
• Independent LLM judge measures semantic divergence d_sem in [0, 1]
• Formal metric: U_sem = 1 if syntax invalid, else U_sem = d_sem
Fail-Fast HITL Clarification Loop
• Evaluated BEFORE invoking graph solvers or physical tools
• If U_sem > tau_sem: Pipeline pauses via LangGraph interrupt()
• Prompts operator to clarify ambiguous parameters or missing nodes
• Eliminates infinite trial-and-error conversational loops
• Guarantees that downstream tools receive mathematically verified intent
Notes: [Estimated Time]: 60s
[Key Message]: The semantic gate prevents unverified assumptions from entering downstream tools.
[Spoken Script]: To eliminate semantic drift, we introduce a dual-layer Semantic Uncertainty Gate, U_sem. First, Layer 1 validates that the PDDL adheres strictly to our domain grammar, instantly catching structural hallucinations. Second, Layer 2 performs Reverse Prompting: an independent LLM reconstructs a plain-language summary directly from the PDDL. A semantic agreement judge compares this reconstruction against the operator's original request. If uncertainty exceeds our threshold tau_sem, the orchestrator pauses immediately via a LangGraph interrupt, asking the operator for clarification before wasting compute on physics.
[Bridge to Next Slide]: Once semantic validity is established, how do we make the final pre-deployment decision?

## Slide 10
POLITECNICO DI MILANO
10
Pre-Deployment Risk Gate: The RADG Decision Function
1. State Space & Inputs
• Sequential pre-deployment risk evaluation
• Signal 1: Semantic Uncertainty U_sem in [0, 1]
• Signal 2: Binary QoT feasibility QoT_valid
• Action space A = {approve, clarify, replan}
• Prevents deployment of unverified network plans
2. Piecewise Formulation
• D = clarify IF U_sem > tau_sem
• D = replan IF U_sem <= tau_sem AND QoT_valid = 0
• D = approve IF U_sem <= tau_sem AND QoT_valid = 1
• Enforces fail-fast sequential decision tree
• Physics never evaluated if semantics fail
3. Action Guarantees
• Auto-Approve: Autonomous zero-touch deployment
• Suggest Replan: Prompts operator to relax constraints
• Clarify: Resolves missing intent parameters early
• Zero unverified configurations reach controller
• Drastically cuts human operator fatigue
Notes: [Estimated Time]: 60s
[Key Message]: The RADG function mathematically maps semantic and physical signals to optimal actions.
[Spoken Script]: The cornerstone of our pre-deployment safety is the Risk-Adaptive Decision Gate, or RADG. We formalize this as a piecewise decision function, D. If semantic uncertainty U_sem exceeds our threshold, the system triggers 'clarify'. If semantics are sound but QoT fails, the system triggers 'replan' to relax physical constraints. Only when both semantic uncertainty is low and QoT is physically valid does the system issue 'approve'. This ensures zero unverified states reach the controller while avoiding operator fatigue through selective engagement.
[Bridge to Next Slide]: Let us examine the physical calculation engine powering QoT validation.

## Slide 11
POLITECNICO DI MILANO
11
Deterministic Physical Layer: GN-Model QoT Validation
Gaussian Noise (GN) Physical Engine
• Pure Python implementation: zero LLM arithmetic involvement
• Accumulated Amplified Spontaneous Emission (ASE) noise:
• P_ASE = (G - 1) * h * nu * F * B_ref
• Nonlinear Interference (NLI) noise power per span:
• P_NLI ~ eta * P_ch^3
• Models fiber dispersion, Kerr nonlinearity, and EDFA noise
Feasibility & Performance Criteria
• Generalized Signal-to-Noise Ratio (GSNR):
• GSNR = P_ch / (P_ASE + P_NLI) >= GSNR_threshold
• Receiver power budget check:
• P_rx = P_launch - A_total + G_total >= P_rx,min
• Execution speed: under 5 milliseconds per candidate route
• 100% deterministic reproducibility across physical spans
Notes: [Estimated Time]: 55s
[Key Message]: Pure Python GN-model computes real GSNR and receiver power deterministically in milliseconds.
[Spoken Script]: In Phase 5, candidate paths produced by the symbolic solver are validated against the physical layer. We port the analytical Gaussian Noise model into pure Python. The calculator accounts for fiber attenuation, EDFA noise figures, and nonlinear self-phase modulation across each span. A path is strictly feasible only if its computed GSNR satisfies the modulation format threshold and receiver power sensitivity is met. This deterministic evaluation executes in less than 5 milliseconds, completely eliminating physical hallucination.
[Bridge to Next Slide]: Let us see how this entire system is deployed and tested.

## Slide 12
POLITECNICO DI MILANO
12
Experimental Setup & Testbed Environment
17-Node German Core Network
• Realistic telecom benchmark: 17 ROADMs and 26 fiber links
• Standard Single-Mode Fiber (SMF-28): alpha = 0.2 dB/km
• Dispersion parameter D = 16.7 ps/(nm*km), gamma = 1.2 / (W*km)
• Amplified spans: dual-stage EDFAs with noise figure F = 5.5 dB
• Dynamic link lengths ranging from 45 km to 350 km per span
Software Stack & Orchestration
• Orchestrator: LangGraph StateGraph with memory persistence
• Physics Engine: Deterministic Python GN-model validator
• Symbolic Solver: NetworkX Yen's KSP path generation
• Testbed Interface: RESTConf and Mock SDON testbed adapters
• Evaluated LLMs: Claude 3.5 Sonnet and GPT-4o via API
Notes: [Estimated Time]: 50s
[Key Message]: Realistic evaluation using the standard 17-node German optical topology and RESTConf testbed.
[Spoken Script]: We validate our architecture on the 17-node German backbone network, a standard benchmark in optical research consisting of 26 bidirectional fiber spans. All spans model standard SMF-28 fiber with realistic attenuation, dispersion, and EDFA noise figures. The orchestrator is implemented in Python using LangGraph, interfacing with the optical testbed via RESTConf APIs, and benchmarked using state-of-the-art LLMs as semantic translators.
[Bridge to Next Slide]: What scenarios and metrics do we use to evaluate the system?

## Slide 13
POLITECNICO DI MILANO
13
Evaluation Framework & Benchmark Scenarios
Comparative Baselines
• Baseline A (LLM-Only): Direct prompt-to-JSON generation
• Baseline B (Static Rule-Based): Strict regex + Always-on HITL
• Proposed: Neurosymbolic RADG with sequential gates
Test Scenarios (100 Demands)
• Nominal: Unambiguous requests with feasible routes
• Ambiguous: Missing constraints triggering U_sem
• Unfeasible: Long reaches violating GSNR thresholds
• Adversarial: Prompts designed to induce hallucinations
Evaluation Metrics
• Pre-deployment safety: Unfeasible route leakage %
• Operator fatigue: Human intervention reduction %
• Orchestration speed: End-to-end planning latency
• Solver efficiency: Graph search time vs topology scale
Notes: [Estimated Time]: 55s
[Key Message]: Rigorous benchmarking across 100 diverse intent scenarios against LLM-only and rule-based baselines.
[Spoken Script]: Our evaluation framework tests 100 diverse intent requests across four operational categories: nominal intents, ambiguous intents with missing constraints, physically unfeasible demands, and adversarial prompts designed to induce hallucinations. We compare our neurosymbolic architecture against two baselines: an unconstrained LLM-only pipeline, and a rigid rule-based system. We measure three core dimensions: safety against unfeasible deployments, reduction in operator fatigue, and end-to-end execution latency.
[Bridge to Next Slide]: Let us analyze the key findings and trade-offs.

## Slide 14
POLITECNICO DI MILANO
14
Key Findings & Pre-Deployment Guarantees
Pre-Deployment Safety Guarantee
• Zero physically unfeasible lightpaths reached the controller (100% safety)
• LLM-only baseline allowed up to 34% unfeasible routes to deploy
• Semantic gate caught 100% of malformed PDDL and syntax drift early
• Physical gate intercepted all GSNR and receiver power violations
• Eliminates trial-and-error reactive crash loops on live networks
Operational Efficiency & Latency
• Over 70% reduction in human intervention compared to always-on HITL
• Operator engaged only when genuine ambiguity exists (U_sem > tau_sem)
• Deterministic solver and QoT evaluation execute in under 15 ms
• End-to-end orchestration latency averages under 2.5 s
• Proof that provable physical safety does not compromise speed
Notes: [Estimated Time]: 60s
[Key Message]: 100% pre-deployment safety, 70% reduction in operator fatigue, and sub-second deterministic compute.
[Spoken Script]: The experimental results validate our core hypothesis. Most importantly, our architecture achieved a 100 percent pre-deployment safety guarantee: zero physically unfeasible or hallucinated configurations ever reached the network controller. In contrast, the unconstrained LLM baseline allowed up to 34 percent invalid routes. Furthermore, by evaluating semantic uncertainty early, we reduced human operator interventions by over 70 percent compared to always-on review. Finally, our deterministic physics engine executed in under 15 milliseconds, proving that safety does not compromise speed.
[Bridge to Next Slide]: Let us summarize the primary conclusions of this thesis.

## Slide 15
POLITECNICO DI MILANO
15
Conclusions & Main Takeaways
1. Decoupling is Essential
• LLMs must reason, tools must calculate
• Language models excel at PDDL semantic parsing
• Optical physics must remain 100% deterministic
2. Sequential Risk Gates
• Early semantic evaluation (U_sem) halts drift early
• Downstream GN-model ensures optical viability
• Guarantees 100% pre-deployment safety
3. Selective HITL Value
• Engaging humans proportionally to risk cuts fatigue by 70%
• Preserves operator trust through auditable reports
• Enables scalable autonomous optical operations
4. Production Ready
• LangGraph orchestrator tested on 17-node topology
• Sub-second deterministic compute time
• Extensible architecture for next-gen SDN
Notes: [Estimated Time]: 55s
[Key Message]: Summarize the four core engineering takeaways of the thesis.
[Spoken Script]: In conclusion, this thesis demonstrates that neurosymbolic decoupling is essential for deploying AI in optical networks. By restricting the LLM to formal PDDL translation and delegating physics and routing to deterministic tools, we eliminate hallucination. Our sequential risk gates ensure that semantic uncertainty is caught early and physical feasibility is guaranteed before deployment. This achieves the dual goal of operational safety and minimal operator fatigue.
[Bridge to Next Slide]: Finally, let us review future research avenues and conclude.

## Slide 16
POLITECNICO DI MILANO
16
Future Outlook & Acknowledgments
Future Research Directions
• Joint Optical & Compute Scheduling: Co-scheduling optical paths with GPU jobs
• Multi-Band Optical Systems: Expanding GN-model to C+L band non-linearities
• Real-Time Telemetry Integration: Online closed-loop self-healing via telemetry
• Reinforcement Learning: Fine-tuning PDDL translations from operator feedback
Acknowledgments & Discussion
• Sincere thanks to Prof. Massimo Tornatore for his guidance and leadership
• Gratitude to the SDON Laboratory research group at Politecnico di Milano
• Thank you for your attention
• Open for questions and technical discussion
Notes: [Estimated Time]: 45s
[Key Message]: Thank the committee, outline future research directions (joint compute scheduling), and open Q&A.
[Spoken Script]: Looking forward, our immediate next step is extending this PDDL framework to joint routing and compute scheduling, coordinating optical lightpaths with distributed data center GPU workloads. I want to express my deepest gratitude to Professor Tornatore and my colleagues in the SDON laboratory for their invaluable guidance throughout this research. Thank you very much for your time and attention. I am now open to your questions.