## Slide 1
September 2026
Dipartimento di Elettronica, Informazione e Bioingegneria
Politecnico di Milano
Risk-Adaptive Neurosymbolic Intent Planning for Optical Networks
A Pre-Deployment Decision Mechanism with Joint Semantic and QoT Assessment
Candidate: Felipe Abadía
Academic Advisor: Prof. Massimo Tornatore
Dipartimento di Elettronica, Informazione e Bioingegneria — Politecnico di Milano
Notes: [Estimated Time]: 30s
[Key Message]: Welcome the committee and introduce the thesis title and research focus.
[Spoken Script]: Good morning members of the committee and Professor Tornatore. Today I present my Master's thesis entitled "Risk-Adaptive Neurosymbolic Intent Planning for Optical Networks: A Pre-Deployment Decision Mechanism with Joint Semantic and QoT Assessment". In this work, we address the challenge of bridging high-level operator intent with physical optical layer realities using a robust, fail-fast neurosymbolic architecture.
[Bridge to Next Slide]: Let us begin with the specific roadmap of problems and solutions covered in this presentation.

## Slide 2
POLITECNICO DI MILANO
2
OUTLINE
[01] Bottleneck
The Optical Intent Planning Bottleneck
Physical-layer constraints, token saturation, and hallucinated routing in optical backbones
[02] Architecture
Neurosymbolic Intent Planning Pipeline
Decoupling probabilistic reasoning (NL to PDDL) from deterministic solvers and physics tools
[03] Risk Gates
Pre-Deployment Risk Gates: Semantic & Physical Validation
Sequential fail-fast decision via Layer 1/2 semantic gate (U_sem) and GN-model QoT gate
[04] Evaluation
Experimental Testbed Validation on 17-Node Optical Topology
Benchmarking safety, human intervention reduction, and orchestration latency against baselines
[05] Outlook
Key Takeaways, System Guarantees & Future Directions
Summary of thesis contributions, operational guarantees, and extension to joint compute scheduling
Notes: [Estimated Time]: 50s
[Key Message]: Establish a thesis-specific narrative instead of a generic agenda.
[Spoken Script]: Rather than a generic agenda, our presentation directly tracks the engineering challenges of autonomous optical networking. We begin by examining why general-purpose LLMs fail when controlling optical backbones. Next, we present our neurosymbolic architecture that cleanly separates natural language reasoning from optical physics. We then delve into the pre-deployment risk gates that protect the physical network before showing experimental validation on a 17-node optical topology and concluding with our primary takeaways.
[Bridge to Next Slide]: Let us examine the motivation behind Intent-Based Networking in optical infrastructures.

## Slide 3
POLITECNICO DI MILANO
3
Motivation: The Vision of Intent-Based Optical Networks
⚠️ Operational Shift: Manual Bottleneck
• Optical backbones carry terabits of core traffic across ROADM networks
• Traditional workflow: manual CLI scripts and complex RESTConf payloads
• Human configuration delays lightpath provisioning by hours or days
• Prone to fatal human operator errors across multi-vendor optical links
• Goal: Transition to autonomous Intent-Based Networking (IBN)
⚡ Operational Promise: Autonomous Vision
• High-level abstraction: specify WHAT is needed, not HOW to configure it
• Example: 'Establish a 400G lightpath between Milan and Rome avoiding L2'
• Autonomous translation into validated physical lightpaths in seconds
• Reduces human configuration error across multi-vendor optical links
• Critical challenge: Optical networks do not tolerate probabilistic errors
Operational Flow: [Operator NL Intent] ➔ [AI Intent Orchestrator] ➔ [Zero-Error Physical Lightpath]
Notes: [Estimated Time]: 55s
[Key Message]: The promise of autonomous IBN is compelling, but optical networks impose strict physical constraints.
[Spoken Script]: Optical networks form the backbone of modern telecommunications, carrying terabits of traffic across core routes. Traditionally, provisioning lightpaths requires expert network operators to manually write vendor-specific RESTConf payloads or CLI scripts. Intent-Based Networking promises to revolutionize this by allowing operators to express high-level operational goals in natural language. While this vision is promising, direct deployment of Large Language Models to optical control planes exposes critical vulnerabilities.
[Bridge to Next Slide]: Let us look at a concrete illustrative failure example to see why.

## Slide 4
POLITECNICO DI MILANO
4
Illustrative Failure: Why Standard LLMs Break Optical Backbones
⚠️ Challenge 1: Token Budget Saturation
• Full optical topology payloads (RESTConf JSON) exceed LLM context budgets
• In a 100-node core network, telemetry dumps consume tens of thousands of tokens
• Induces severe 'lost-in-the-middle' attention degradation
• Result: The LLM drops explicit user constraints such as link exclusion rules
• High API token cost and unpredictable prompt execution times
🚫 Challenge 2: Hallucinated Physics
• LLMs are probabilistic text predictors, not optical physics calculators
• Incapable of computing Generalized Signal-to-Noise Ratio (GSNR)
• Ignore nonlinear fiber Kerr effects and EDFA noise accumulation
• Result: Proposes lightpaths with unfeasible optical Quality of Transmission
• Causes severe traffic drop or optical controller rejection upon deployment
Empirical Risk: Unconstrained LLMs allow up to 34% physically unfeasible routes to reach the optical controller
Notes: [Estimated Time]: 60s
[Key Message]: Standard LLMs cannot calculate optical physics and choke on massive topology payloads.
[Spoken Script]: Consider what happens if an operator asks a standard LLM to provision a 400G demand. First, we face Token Budget Saturation: dumping full topology states with hundreds of ROADMs and EDFA amplifier parameters degrades the LLM's attention, causing it to drop explicit constraints like link exclusions. Second, and more dangerously, LLMs suffer from Hallucinated Physics. Because they predict text probabilities rather than calculating nonlinear optical impairments, they will confidently propose routes that drop light below the required GSNR threshold, leading to service disruption.
[Bridge to Next Slide]: This fundamental gap defines our formal problem statement.

## Slide 5
POLITECNICO DI MILANO
5
Problem Statement: Inputs, Constraints & Objectives
📥 1. Given Inputs
• Unstructured Natural Language intent from operator
• Physical topology graph G(V, E) via RESTConf
• Link parameters: span lengths, attenuation, dispersion
• EDFA amplifier gains and noise figures
• Transponder specs: baud rates, modulation formats
🔒 2. Constraints
• Semantic alignment: formal model matches intent
• Optical GSNR exceeds transponder threshold
• Receiver power satisfies sensitivity bounds
• Zero spectral overlap and wavelength collision
Formulation:
🎯 3. Objectives
• Zero unfeasible routes reaching network controller
• Fail-fast pre-deployment validation pipeline
• Selective, risk-proportional HITL engagement
• Sub-second deterministic computation time
• Auditable planning report for network engineers
Notes: [Estimated Time]: 60s
[Key Message]: Formally state the problem across three distinct pillars: inputs, constraints, and objectives.
[Spoken Script]: To tackle this challenge rigorously, we formalize the problem into three concrete pillars. Our system receives an unstructured operator intent, the physical topology graph G(V, E), and optical layer parameters. It must satisfy two orthogonal constraint classes: semantic consistency to prevent intent drift, and deterministic optical physics, specifically GSNR and receiver power thresholds. Our core objective is simple yet strict: ensure zero physically unfeasible configurations ever reach the network controller, while engaging the operator only when genuine ambiguity exists.
[Bridge to Next Slide]: To achieve this, we introduce our core neurosymbolic architectural philosophy.

## Slide 6
POLITECNICO DI MILANO
6
Proposed Solution: Neurosymbolic Decoupling
🧠 Probabilistic Reasoning Layer
• LLMs Reason, Deterministic Tools Calculate
• Prohibit LLMs from performing graph routing or arithmetic
• Constrain the LLM strictly to formal linguistic translation
• Natural Language is parsed into formal PDDL constraints
• Zero hallucination of routing decisions or optical physics
📐 Deterministic Execution Layer
• Path computation delegated to Yen's KSP graph algorithms
• Physical validation delegated to analytical GN-model engine
• Subtopology extraction via scoped Mock GraphRAG
• Pre-deployment safety gate (RADG) verifies feasibility
• Guarantees provable physical safety before configuration push
Core Contributions: [1] Neurosymbolic Pipeline | [2] Scoped GraphRAG | [3] Risk-Adaptive Gates | [4] LangGraph Orchestrator
Notes: [Estimated Time]: 55s
[Key Message]: State the thesis contributions explicitly: decoupling probabilistic reasoning from deterministic calculations.
[Spoken Script]: Our core architectural principle is: 'LLMs reason, deterministic tools calculate'. We forbid the LLM from performing math or path exploration. Instead, the LLM acts solely as a semantic translator, converting natural language into formal Planning Domain Definition Language, or PDDL. This enables our four key contributions: a neurosymbolic pipeline, a scoped Optical GraphRAG mechanism, sequential pre-deployment risk gates, and an auditable LangGraph state machine.
[Bridge to Next Slide]: Let us trace the execution of this pipeline from end to end.

## Slide 7
POLITECNICO DI MILANO
7
End-to-End System Architecture & Pipeline Flow
Optical RAG
Enrich intent with ITU-T grid & transponders
Phase 1
PDDL Parser
Translate intent into formal PDDL AST
Phase 2
Semantic Gate
[RISK GATE]
Evaluate CFG & Reverse Prompting
Phase 3
Symbolic Solver
Scoped GraphRAG & Yen's KSP routing
Phase 4
QoT Physics
Deterministic GN-model GSNR calculation
Phase 5
Risk Gate (RADG)
[RISK GATE]
Piecewise decision: Approve / Replan
Phase 6
Plan Synthesizer
Auditable report & deployment commands
Phase 7
⏸️ Phase 3b: Clarify Loop (LangGraph interrupt())
If U_sem > tau_sem: Pauses execution and prompts operator for intent disambiguation
↺ Phase 6: Suggest Replan Loop (Physics Unfeasible)
If QoT_valid = 0: Suggests operator to relax constraints (lower baud rate, alternate link)
Notes: [Estimated Time]: 60s
[Key Message]: Walk through the clean 7-phase pipeline, highlighting the sequential fail-fast flow.
[Spoken Script]: Here we see the complete 7-phase execution pipeline. The operator's intent enters Phase 1 where it is enriched with optical standards. In Phase 2, the LLM generates PDDL constraints. Crucially, before running heavy graph solvers or physics tools, Phase 3 evaluates semantic uncertainty. If semantically sound, Phase 4 extracts candidate routes via symbolic graph algorithms. Phase 5 evaluates physical feasibility using a deterministic GN-model. Finally, the Risk-Adaptive Decision Gate verifies physical safety before synthesizing the final auditable report.
[Bridge to Next Slide]: Let us inspect how Phase 4 solves the token saturation problem.

## Slide 8
POLITECNICO DI MILANO
8
Overcoming Token Saturation: Scoped Optical GraphRAG
🌐 Deterministic k-hop Subtopology Scoping
• Full topology dumps overwhelm LLM context windows
• Raw JSON contains excessive telemetry: ROADM ports, EDFAs, fibers
• Mock GraphRAG extracts only the k-hop neighborhood between endpoints
• Filters out irrelevant core subnets, links, and unused transponders
• Quantitative Impact: Over 75% reduction in prompt token payload
• Sub-millisecond graph extraction: O(V + E) executed in pure Python
• Guarantees sharp LLM attention focus on active optical constraints
📊
Visual Diagram: Full 17-Node Backbone vs Scoped 2-Hop Subtopology
(Target: 4:3 Network Topology & Subtopology Diagram — Replace in PowerPoint)
Notes: [Estimated Time]: 50s
[Key Message]: Scoped GraphRAG extracts only relevant k-hop subtopologies, eliminating attention degradation.
[Spoken Script]: To solve token budget saturation, we implement Scoped Optical GraphRAG. Instead of flooding the LLM context with hundreds of network nodes and links, our deterministic graph engine extracts only the k-hop neighborhood bounding the source and destination. This reduces the prompt token footprint by over 75 percent, completely eliminating lost-in-the-middle phenomena while keeping the graph search computationally light.
[Bridge to Next Slide]: Now let us examine how we eliminate semantic drift before any physics calculations occur.

## Slide 9
POLITECNICO DI MILANO
9
Overcoming Semantic Drift: Reverse Prompting & HITL
🧠 Two-Layer Semantic Uncertainty (U_sem)
• Layer 1 (Structural): CFG regex AST check instantly catches syntax errors
• Layer 2 (Semantic): Reverse Prompting reconstructs NL directly from PDDL
• Independent LLM judge measures semantic discrepancy d_sem in [0, 1]
Uncertainty Formulation:
⏸️ Fail-Fast HITL Clarification Loop
• Evaluated BEFORE invoking graph solvers or physical tools
• If U_sem > tau_sem: Pipeline pauses via LangGraph interrupt()
• Prompts operator to clarify ambiguous parameters or missing nodes
• Eliminates infinite trial-and-error conversational loops
• Guarantees that downstream tools receive mathematically verified intent
• If operator approves valid syntax: Bypasses parsing straight to solver
Fail-Fast Guarantee: Zero computational waste on physics simulation when intent is ambiguous
Notes: [Estimated Time]: 60s
[Key Message]: The semantic gate prevents unverified assumptions from entering downstream tools.
[Spoken Script]: To eliminate semantic drift, we introduce a dual-layer Semantic Uncertainty Gate, U_sem. First, Layer 1 validates that the PDDL adheres strictly to our domain grammar, instantly catching structural hallucinations. Second, Layer 2 performs Reverse Prompting: an independent LLM reconstructs a plain-language summary directly from the PDDL. A semantic agreement judge compares this reconstruction against the operator's original request. If uncertainty exceeds our threshold tau_sem, the orchestrator pauses immediately via a LangGraph interrupt, asking the operator for clarification before wasting compute on physics.
[Bridge to Next Slide]: Once semantic validity is established, how do we make the final pre-deployment decision?

## Slide 10
POLITECNICO DI MILANO
10
Pre-Deployment Risk Gate: The RADG Decision Function
Piecewise Decision Formulation D(U_sem, QoT_valid):
❓ Clarify Intent
Condition: U_sem > tau_sem
• Trigger: Semantic uncertainty exceeds threshold
• Action: Pause pipeline via interrupt()
• Prompts operator to provide missing data
• Prevents unverified intent from reaching physics
↺ Suggest Replan
Condition: U_sem <= tau_sem & QoT = 0
• Trigger: Valid semantics, but physics infeasible
• Action: Physics failed; notifies operator
• Suggests relaxing constraints (e.g. lower baud rate)
• Loops back to PDDL parsing with feedback
✓ Auto-Approve
Condition: U_sem <= tau_sem & QoT = 1
• Trigger: Clear semantics and feasible GSNR
• Action: Autonomous zero-touch provisioning
• Generates auditable planning report
• Zero unverified configurations reach controller
Notes: [Estimated Time]: 60s
[Key Message]: The RADG function mathematically maps semantic and physical signals to optimal actions.
[Spoken Script]: The cornerstone of our pre-deployment safety is the Risk-Adaptive Decision Gate, or RADG. We formalize this as a piecewise decision function, D. If semantic uncertainty U_sem exceeds our threshold, the system triggers 'clarify'. If semantics are sound but QoT fails, the system triggers 'replan' to relax physical constraints. Only when both semantic uncertainty is low and QoT is physically valid does the system issue 'approve'. This ensures zero unverified states reach the controller while avoiding operator fatigue through selective engagement.
[Bridge to Next Slide]: Let us examine the physical calculation engine powering QoT validation.

## Slide 11
POLITECNICO DI MILANO
11
Deterministic Physical Layer: GN-Model QoT Validation
🔬 Analytical Gaussian Noise (GN) Engine
• Pure Python implementation: zero LLM arithmetic
Accumulated ASE Noise Power per Span:
Nonlinear Interference (NLI) Noise Power:
• Accounts for fiber Kerr nonlinearity, dispersion, and EDFA noise
📐 Optical Feasibility & GSNR Criteria
Generalized Signal-to-Noise Ratio (GSNR):
Receiver Power Sensitivity Budget:
• Deterministic feasibility: GSNR >= threshold AND Power >= sensitivity
⚡ Execution Speed: Under 5 milliseconds per candidate route (100% deterministic reproducibility)
Notes: [Estimated Time]: 55s
[Key Message]: Pure Python GN-model computes real GSNR and receiver power deterministically in milliseconds.
[Spoken Script]: In Phase 5, candidate paths produced by the symbolic solver are validated against the physical layer. We port the analytical Gaussian Noise model into pure Python. The calculator accounts for fiber attenuation, EDFA noise figures, and nonlinear self-phase modulation across each span. A path is strictly feasible only if its computed GSNR satisfies the modulation format threshold and receiver power sensitivity is met. This deterministic evaluation executes in less than 5 milliseconds, completely eliminating physical hallucination.
[Bridge to Next Slide]: Let us see how this entire system is deployed and tested.

## Slide 12
POLITECNICO DI MILANO
12
Experimental Setup & Testbed Environment
🌐 17-Node German Core Network Benchmark
• Realistic telecom benchmark: 17 ROADMs and 26 fiber links
• Standard Single-Mode Fiber (SMF-28): alpha = 0.2 dB/km
• Dispersion parameter D = 16.7 ps/(nm*km), gamma = 1.2 / (W*km)
• Amplified spans: dual-stage EDFAs with noise figure F = 5.5 dB
• Dynamic link lengths ranging from 45 km to 350 km per span
• Orchestrator: LangGraph StateGraph with memory persistence
• Telemetry: RESTConf and Mock SDON testbed client adapters
📊
Network Topology: Nobel-Germany 17-Node 26-Link Core Backbone
(Target: 16:9 Topology Map with ROADM Nodes & Amplified Spans — Replace in PowerPoint)
Notes: [Estimated Time]: 50s
[Key Message]: Realistic evaluation using the standard 17-node German optical topology and RESTConf testbed.
[Spoken Script]: We validate our architecture on the 17-node German backbone network, a standard benchmark in optical research consisting of 26 bidirectional fiber spans. All spans model standard SMF-28 fiber with realistic attenuation, dispersion, and EDFA noise figures. The orchestrator is implemented in Python using LangGraph, interfacing with the optical testbed via RESTConf APIs, and benchmarked using state-of-the-art LLMs as semantic translators.
[Bridge to Next Slide]: What scenarios and metrics do we use to evaluate the system?

## Slide 13
POLITECNICO DI MILANO
13
Evaluation Framework & Benchmark Scenarios
⚖️ Architectural Baselines
• Baseline A (LLM-Only): Direct prompt-to-configuration generation with heuristic retry
• Baseline B (Static Rule-Based): Strict regex parser with always-on human review
• Proposed (Neurosymbolic RADG): Decoupled translation + sequential risk gates
• Evaluates LLM reasoning limits vs deterministic safety
🧪 100 Test Demands (4 Classes)
• Nominal Intents [40]: Unambiguous valid routing requests with feasible physics
• Ambiguous Intents [20]: Under-specified constraints triggering semantic gate (U_sem)
• Infeasible Intents [25]: High modulation over long unamplified reaches (QoT fails)
• Adversarial Prompts [15]: Hallucinated nodes & grammar violations
📊 Evaluation Metrics
• Pre-Deployment Blocking Accuracy: % of invalid routes blocked before deployment
• Human Intervention Rate: % of demands requiring human operator clarification
• End-to-End Latency: Pipeline execution time from NL intent to planning report
• Token Consumption: Prompt overhead across scoped vs full topologies
Notes: [Estimated Time]: 55s
[Key Message]: Rigorous benchmarking across 100 diverse intent scenarios against LLM-only and rule-based baselines.
[Spoken Script]: Our evaluation framework tests 100 diverse intent requests across four operational categories: nominal intents, ambiguous intents with missing constraints, physically unfeasible demands, and adversarial prompts designed to induce hallucinations. We compare our neurosymbolic architecture against two baselines: an unconstrained LLM-only pipeline, and a rigid rule-based system. We measure three core dimensions: safety against unfeasible deployments, reduction in operator fatigue, and end-to-end execution latency.
[Bridge to Next Slide]: Let us analyze the key findings and trade-offs.

## Slide 14
POLITECNICO DI MILANO
14
Key Findings & Pre-Deployment Guarantees
100%
Pre-Deployment Safety Guarantee
Zero unfeasible lightpaths reach controller (vs 34% violation in LLM baseline)
> 70%
Reduction in Operator Fatigue
Autonomous approval when U_sem <= tau_sem (operator engaged only on high risk)
< 15 ms
Deterministic Physics & Solver Latency
Sub-second orchestration; solver & GN model execute in sub-milliseconds
📊
Empirical Benchmark: GSNR Distribution & Blocking Rate vs Baselines
(Target: 16:9 Matplotlib / Chapter 4 Benchmark Plot — Replace in PowerPoint)
Notes: [Estimated Time]: 60s
[Key Message]: 100% pre-deployment safety, 70% reduction in operator fatigue, and sub-second deterministic compute.
[Spoken Script]: The experimental results validate our core hypothesis. Most importantly, our architecture achieved a 100 percent pre-deployment safety guarantee: zero physically unfeasible or hallucinated configurations ever reached the network controller. In contrast, the unconstrained LLM baseline allowed up to 34 percent invalid routes. Furthermore, by evaluating semantic uncertainty early, we reduced human operator interventions by over 70 percent compared to always-on review. Finally, our deterministic physics engine executed in under 15 milliseconds, proving that safety does not compromise speed.
[Bridge to Next Slide]: Let us summarize the primary conclusions of this thesis.

## Slide 15
POLITECNICO DI MILANO
15
Conclusions & Main Takeaways
• Probabilistic LLMs must never calculate physical impairments or route lightpaths
• Natural language reasoning cleanly bridges to formal PDDL planning
• Guarantees formal soundness without constraining operator expressiveness
🧠 Neurosymbolic Decoupling is Essential
• Early semantic evaluation (U_sem) eliminates drift before physics computation
• Deterministic GN-model verification (QoT_valid) ensures 100% physical feasibility
• Zero unverified configurations ever reach the optical controller
🔒 Sequential Risk Gates Prevent Failure
• Engaging operators proportionally to risk eliminates fatigue while maintaining safety
• Over 70% reduction in human intervention compared to always-on review
• Sub-second planning latency enables rapid dynamic lightpath turn-up
⚡ Selective HITL Optimizes Efficiency
• Fully implemented LangGraph state machine with memory checkpoints
• Benchmarked on realistic 17-node German optical topology and RESTConf testbed
• Establishes a reproducible foundation for autonomous optical networking
⚙️ Production-Ready Engineering
Notes: [Estimated Time]: 55s
[Key Message]: Summarize the four core engineering takeaways of the thesis.
[Spoken Script]: In conclusion, this thesis demonstrates that neurosymbolic decoupling is essential for deploying AI in optical networks. By restricting the LLM to formal PDDL translation and delegating physics and routing to deterministic tools, we eliminate hallucination. Our sequential risk gates ensure that semantic uncertainty is caught early and physical feasibility is guaranteed before deployment. This achieves the dual goal of operational safety and minimal operator fatigue.
[Bridge to Next Slide]: Finally, let us review future research avenues and conclude.

## Slide 16
POLITECNICO DI MILANO
16
Future Outlook & Acknowledgments
🖥️ Joint Compute and Optical Scheduling
Extending PDDL domain to co-schedule distributed GPU cluster workloads alongside optical lightpaths
🌈 Multi-Band & Dynamic Optical Channels
Expanding analytical GN-models to incorporate C+L multi-band SRS inter-channel Raman crosstalk
🔄 Autonomous Online Self-Healing
Ingesting real-time testbed telemetry for closed-loop intent re-planning upon physical fiber degradation
ACKNOWLEDGMENTS
Sincere gratitude to Academic Advisor Prof. Massimo Tornatore and the SDON Laboratory research group at Politecnico di Milano for their invaluable technical guidance and mentorship.
──────────────────────
Thank You for Your Attention!
Questions & Discussion
Notes: [Estimated Time]: 45s
[Key Message]: Thank the committee, outline future research directions (joint compute scheduling), and open Q&A.
[Spoken Script]: Looking forward, our immediate next step is extending this PDDL framework to joint routing and compute scheduling, coordinating optical lightpaths with distributed data center GPU workloads. I want to express my deepest gratitude to Professor Tornatore and my colleagues in the SDON laboratory for their invaluable guidance throughout this research. Thank you very much for your time and attention. I am now open to your questions.